## Slide 1: Inventory accuracy Cycle Count and PI
Notes: Welcome!
-We are taking attendance; if more than one person on the line, please enter the names in the Chat window or send to the facilitator. Please encourage your colleagues to attend one of the remaining sessions.
-Ask that you mute your phone and post any questions throughout the session into the Chat window; we are keeping a parking lot for questions
Add picture that represents the topic, then update Title and Date
Sources for pictures include:
Adient Brand Center > Brand Imagery: http://www.adient-brand.com/adient/assets?assetTypes%5B%5D=imagery
Knowledge Management Image Library: https://connect.adient.com/sites/sapcommunity/ef/PublishingImages/Forms/Thumbnails.aspx?InitialTabId=Ribbon%2ERead&VisibilityContext=WSSTabPersistence
Internet keyword search/Images
Replace picture with one that represents the topic, then update Business Unit, Title and Date

## Slide 2: Cycle Counting
Item ABC classification
    Print Cycle count worksheet
    Cycle count results entry
    Cycle count results entry (Recount)

## Slide 3: Learning objectives
Upon completion of this course, you should be able to:
    Understand ABC classification
    Print Cycle count worksheet
    Cycle count results entry
    Cycle count results entry (Recount)
Notes: Example: Use these kinds of action verbs for what the participant is expected to do after learning takes place

## Slide 4: Cycle Counting
Item ABC classification
    Print Cycle count worksheet
    Cycle count results entry
    Cycle count results entry (Recount)

## Slide 5: Cycle counting
    1.5.9 Item ABC Status Report/Update
    3.13.1 Print Cycle count worksheet
    3.13.2 Cycle count results entry (Initial)
    3.13.2 Cycle count results entry (Recount)
Notes: Enter title of topic and bulleted list of subtopics
Optional: Replace picture with one that is relevant to the topic

## Slide 6: Process Flow – Cycle Counting
Notes: Click to add text or other content types
Use tables to show what is changing, terms, roles & responsibilities, etc.
TIP: Click on the table and a TABLE TOOLS ribbon displays other design/layout options for the table

## Slide 7: Item ABC Status Report/Update
In order to let the system automatically create worklist for usage in the cycle count process, the ABCDE classification needs to be maintained in Item Inventory Data maintenance screen

## Slide 8: Cycle count worksheet print
This program can be used to print out worksheet where results can be easily signed in. It is possible to set up what items should be counted by many different parameters as needed.

## Slide 9: Cycle count results entry (Initial)
You can enter the results as an “Initial” or a “Recount”. The default is Initial. If the cycle count type is Initial, the qty on hand is compared to the count quantity. If the difference is WITHIN the allowed error tolerance, the item quantity on hand is UPDATED to the count value.
.

## Slide 10: Cycle count results entry (Recount)
In order to enter the “Recount”, the default value needs to be changed to “Recount”. When we post the recounted quantity on hand, it is NOT compared to the count quantity. Regardless of the difference of quantity on hand compared to the item quantity on hand is updated to the count value. A message will be displayed as well (WARNING: Count is out of tolerance.)
Imp Fields:
Cycle Count Type: State whether this is an Initial or a Recount
Item Number: Item counted
Site: This is the SITE where you counted the part.
Location: This is the LOCATION in which you counted the part.

## Slide 11: Physical Inventory
    Delete old Tags
    Delete/Archive Zero Balance
    Freeze Inventory Balance
    Feed stock count details back to system
    Verify Inventory Variance
    Update Inventory Balance

## Slide 12: Physical Inventory
    3.16.23: Tag Delete/Archive
    3.23: Zero Balance Delete/Archive
    3.16.4: Inventory Balance Freeze
    3.16.1; 3.16.2; 3.16.6: Create and Print Tags
    3.16.11: Item Tag Count Entry:
    3.16.14: Counted Tag Report
    3.16.15: Uncounted Tag Report
    3.16.7: Tag Void Status Update
    3.16.18: Print Inventory Variance Report:
    3.16.12: Item Tag Recount Entry
    3.16.21: Inventory Balance Update
Notes: Enter title of topic and bulleted list of subtopics
Optional: Replace picture with one that is relevant to the topic

## Slide 13: Process Flow – Physical Inventory
Notes: Click to add text or other content types
Use tables to show what is changing, terms, roles & responsibilities, etc.
TIP: Click on the table and a TABLE TOOLS ribbon displays other design/layout options for the table

## Slide 14: Tag Delete / Archive
Tag Delete/Archive is the first step in the physical inventory process. Use Tag Delete/Archive to delete and archive physical inventory tags, usually ones from the last count that are no longer needed.

## Slide 15: Tag Delete / Archive

## Slide 16: Delete Zero Balance Report
Use Zero Balance Delete/Archive to remove the inventory detail information for any item, site, location, lot/serial, and lot reference combination with zero quantity currently on hand.

## Slide 17: Inventory Balance Freeze
Use the Inventory Balance Freeze to freeze the existing inventory quantities that will be used in the calculations for inventory adjustments from the physical inventory

## Slide 18: Create and Print Tags
Item Tag Create generates count tags for each inventory detail record

## Slide 19: Create and Print Tags

## Slide 20: Item Tag Count Entry
Enter data for each individual counted physical inventory bulk tag

## Slide 21: Counted Tag Report
Counted Tag reports provides the list of Tags that have been counted

## Slide 22: Uncounted Tag Report
Use this report to determine the uncounted Bulk tag numbers that need to be voided. Any unused bulk tags should then be voided (using 3.16.7)

## Slide 23: Tag Void Status Update
Use this option to void any Bulk tag ranges that were not used in the physical inventory count.

## Slide 24: Print Inventory Variance Report
This report highlights the variance between the Inventory available in the system and physical count. It shows variance %age, variance amount and warnings, if any

## Slide 25: Print Inventory Variance Report

## Slide 26: Item Tag Recount Entry
Used for the correction of tags. Once you enter the initial tag count, it can only be changed using Tag Recount Entry. You can change the count as many times as you like, up until the Inventory Balance Update is run. Recount data will be entered in on the left side of the screen (“recount” fields)

## Slide 27: Inventory Balance Update
Use Inventory Balance Update to adjust inventory balances to reflect the item quantity counted at a given site

## Slide 28: Questions
Notes: Optional: Replace picture with one that is relevant to the topic